## Slide 1: mPlane – Building an Intelligent Measurement Plane for the Internet
Maurizio Dusi – NEC Laboratories Europe
maurizio.dusi@neclab.eu
NSF Workshop on perfSONAR based Multi-domain
Network Performance Measurement and Monitoring
February 20-21, 2014

## Slide 2: The Internet is nowadays a complicated technology…
The internet is a key infrastructure where different technologies are combined to offer a plethora of services. It’s horribly complicated.
We sorely miss the technology to understand what is happening in the network and to optimize its performance and utilization.

## Slide 3: Outline
mPlane: a measurement plane for the Internet
  architecture
mPlane in practice
  DaaS troubleshooting
  Monitoring Akamai CDN

## Slide 4: The EU project mPlane
About the design and demonstration of a measurement plane for the Internet
  A distributed infrastructure for network measurement
  … which perform passive and active measurements, continuously or on-demand, at a wide variety of scales
  … with built-in support for iterative measurement and automated iteration.
16 European partners
In three years! (since 11/2012)
   support easy integration of existing technology
https://www.ict-mplane.eu

## Slide 5: mPlane components
active probe
passive probe
data
control
DBStream
Blockmon

## Slide 6: Architecture Overview
Each component
  advertise capabilities
  perform measurements/ analyses given specifications
  return/export results
Measurements completely defined by the types of data they produce and parameters they require

## Slide 7: Example Capability: ping
capability: measure parameters: start.ms: now...+inf end.ms: now...+inf source.ip4: 10.2.3.4 destination.ip4: * period.s: 1...60 results: - delay.twoway.icmp.ms.min - delay.twoway.icmp.ms.mean - delay.twoway.icmp.ms.max

## Slide 8: Example Specification: ping
specification: measure parameters: start.ms: 2014-01-20 09:25:00 end.ms: 2014-01-20 09:26:00 source.ip4: 10.2.3.4 destination.ip4: 10.4.5.6 period.s: 1 results: - delay.twoway.icmp.ms.min - delay.twoway.icmp.ms.mean - delay.twoway.icmp.ms.max

## Slide 9: Example Result: ping
result: measure parameters: start.ms: 2014-01-20 09:25:01.135 end.ms: 2014-01-20 09:26:01.136 source.ip4: 10.2.3.4 destination.ip4: 10.4.5.6 period.s: 1 results: - delay.twoway.icmp.ms.min - delay.twoway.icmp.ms.mean - delay.twoway.icmp.ms.max resultvalues: - - 39 - 44 - 73

## Slide 10: mPlane workflow: iterative analysis
Repository
Supervisor
Raw data
Setup the system to monitor a service
(e.g., quality of YouTube streaming)
passive probe reports an anomaly
start Root Cause Analysis
  crosscheck with passive probes
  crosscheck on larger time scale
  crosscheck by active probing
  Is because of
    DNS
    Routing
    Others?
Alarm!
Found
Reasoner

## Slide 11: mPlane inter-domain measurements
Each domain collects and owns measurements
Multi-domain measurements handled as communications among supervisors

## Slide 12: mPlane interoperability
We are working on an adapter between mPlane and the tool native interfaces
Using of existing standards
  Measurements as capabilities
    Definitions taken from the IETF IPPM WG
  Partially structured namespace
    [base].[modifiers].[units].[aggregation]: [primitive]

## Slide 13: Some of mPlane use cases
Desktop as a Service troubleshooting
Anomaly detection and root cause analysis in large-scale networks
Quality of Experience for web browsing
Mobile network performance issues
Verification and certification of service-level agreements
Content popularity and caching strategies
FOCUS
FOCUS

## Slide 14
mPlane use case I:
Desktop as a Service troubleshooting

## Slide 15: Desktop as a Service troubleshooting
Detecting the Quality of Experience of users accessing content using Desktop-as-a-Service solutions through thin-client connections

## Slide 16: Workflow
Probes send info about the thin-client connection to the repository
The Reasoner
  classifies the connection (application on top) [1]
  correlates application with network conditions along the path
  monitors users’ QoE
      Poor? start root cause analysis (iterative measurements)
      e.g., migrate virtual server closer to the user
[1] M. Dusi et al., “A closer look at thin-client connections: statistical application identification for QoE detection”, IEEE Communication Magazine, 2012
Alarm!

## Slide 17
mPlane use case II:
Monitoring Akamai CDN

## Slide 18: CDN Daily pattern:
Preferred cache serve ~30% of traffic at peak time
Occasional drop in the preferred chace selection
Abrupt changes trigger the iterative analysis coordinated by the Reasoner

## Slide 19: Shift in the Akamai served traffic
Iterative analysis performed by the reasoner
  Diagnosis performed following a tree-like structure

## Slide 20: Single server issue?
Compute the traffic volume per IP address for every 15m time intervals
40 servers always active handle 62% of traffic
NO

## Slide 21: Service(*) issue?
Select the top 500 services served by Akamai
  Order by frequency
  Repeat for each 5m time interval
NO
(*) Service == FQDN

## Slide 22: CDN performance issues?
For services served by Akamai preferred cache
  Compute the distribution of server elaboration time
    time between the TCP ACK of the HTTP GET and the reception of the first byte of the reply
  Plot percentiles every 5m of time
YES!!
NO!!!

## Slide 23: What else?
Final root cause analysis not identified
  Calls for having mPlane deployed for on-line iterative analysis
  Other vantage points report the same problem
Extending the time period?
Routing?
DNS mapping?
Suggestions?

## Slide 24: Conclusions
mPlane aims at simplifying network monitoring practices
  Supervisor focused on iterative measurements
    Troubleshooting support
  Open source release of software
    Tstat, Blockmon, QoF, tracebox
  Maximum reuse of existing measurement tools
    First software libraries will be released soon
Collaborations are welcome!
Info @ http://www.ict-mplane.eu

## Slide 25: Thanks!
Maurizio Dusi – NEC Laboratories Europe
maurizio.dusi@neclab.eu